NALSAR University of Law

TENDER DOCUMENT

Name of Work:    Annual Maintenance Contract for Sewage Treatment Plant of capacity 150 cum / day at NALSAR University of Law, Shameerpet, Hyderabad.

Document Price: Rs.2,500/- only

NALSAR UNIVERSITY OF LAW,

Post Box No:1, Justice City,

SHAMEERPET,

Medchal-Malkajgiri District,

Hyderabad.

Telangana State. Pin: 500 101

Phone No: 040-23498110

NALSAR UNIVERSITY OF LAW

Post Box No.1, Justice City,

Shameerpet,

Medchal-Malkajgiri Dist,

HYDERABAD-500101.

Phone: 040-23498103/104/115

Fax: 040-23498385/386.

Tender No. NALSAR/STP/07/2021                                                              Date:  02.12.2020

##### Sub: Annual Maintenance Contract and certain repair works for Sewage

##### Treatment Plant of capacity 150 KLD at NALSAR University of Law.

## NALSAR University of law invites sealed quotations in two envelope system from reputed contractors/Agencies for the Operation & Maintenance and certain repair works of Sewerage Treatment Plant as per Terms and Conditions mentioned in the Tender Document.

## Tender form along with terms and conditions, can be collected from Engineering Department Office, NALSAR University of Law, Shameerpet between 09.00 A.M. and 05.00 P.M. on any working day up to 23th December, 2020 on payment of Rs.2,500/- (non-refundable) in the form of DD/ pay order/ banker’s cheque in favour of “Registrar, NALSAR University of Law, Hyderabad”.  The application form can also be downloaded from the University’s website www.nalsar.ac.in and should be sent along with the above requisite fee.

| Last date of submission of tender | 23.12.2020, 03.00 p.m. |
| --- | --- |
| Date of opening of technical bid | 23.12.2020 at 03.30 p.m. |

| S.No. | Particulars | Annexure |
| --- | --- | --- |
| 1 | Certificate | I |
| 2 | Technical Bid Format | II |
| 3 | Format for Price Bid | III |
| 3 | Format for Bid Format | IV |

METHOD OF SUBMISSION OF QUOTATIONS IN TWO ENVELOPE SYSTEM

FIRST ENVELOPE - “Technical Bid” contents following:-

(a)  Subscribe on FIRST ENVELOPE – Technical Bid for “Tender No. NALSAR/STP/07/2020 Due Date 23-12-2020 and write your Company Name & Address at the bottom of envelope for identification.

(b)  EMD by Demand Draft/ or by Cash equivalent of Rs.20,000/-. EMD paid by way of Cheque not acceptable.  Please enclose the Receipt/DD in original favoring Registrar, NALSAR University of Law. If you are depositing Cash then enclose Original Cash Receipt in to this envelope and retain a photocopy of the Cash Receipt with you and Non-refundable Demand Draft of Rs.2500/- may also enclose towards tender processing fee.

(c)  The Tenderer’s Status form (Annexure II) is enclosed with this Enquiry. The form to be filled in indicating your Company profile and signed by your authorized representative and to be attached in the First Envelope – Technical Bid.

(d)  Please note that, Tax related concessional forms like 2B/C/3D/D will not be provided by us.

(e) Please mention whether you are registered with NSIC. (For details, visit www.nsic.co.in/go.asp).   If “YES”, please attach a photo copy of “Registration Certificate”. If “NO”, your bid / quote will not be “Technically rejected”, based on this point.

(f)  Please attach photocopy of PAN Card.

(g)  Mention all present Taxes, Excise, Octroi, which you have considered, their percentage and Amount in Rupees.

(h)  Please confirm that the total amount mentioned in the Commercial Details excludes all the taxes.

  - Please confirm that the quote / price for all the ITEMS have been mentioned in the “Price Bid.”

  - Please confirm that the amount mentioned, in the Price Bid (Kept in the “Envelope Two”) is unconditional in nature. Accordingly, it shall be treated as “Unconditional Offer”.

  - Please confirm that the price is not to be mentioned in the Technical Bid.

  - The format of Declaration/Acceptance undertaking (Annexure I) is also enclosed with this enquiry. The same should be signed by your authorized representative and attached with Technical Bid.

Note:  As part of/along with your Technical Bid, please submit Registration Certificates, Trade and Industry Accreditation, if any as applicable.  NALSAR may visit the facility of Bidders to assess suitability as part of Technical Evaluation of bids.

SECOND ENVELOPE– “Price Bid” will have following:-

(a)  On the SECOND ENVELOPE – write “Tender No. NALSAR/STP/07/2020 Due date      23.12.2020 and also mention your Company’s Name & Address at the bottom of the envelope.

(b)  Please fill up enclosed Price Bid Form (Annexure III) and keep in the Second Envelope– Price Bid. The Price Bid must be signed by your authorized representative bearing Company Stamp.

(c) Alternatively you can use your Company letter head for Price Bid but it has to be typed in the manner/format shown in our Price Bid Form.

CORRECTIONS / OVERWRITINGS IN BIDS: Bidder needs to sign at all these places

THE TWO SEPARATE SEALED ENVELOPES (i.e. ONE ENVELOPE FOR THE TECHNICAL DETAILS, AND SECOND ENVELOPE FOR THE PRICE DETAILS) MAY BE INSERTED IN A MASTER ENVELOPE SUPERSCRIBED WITH “BID FOR TENDER ENQ. NO NALSAR/STP/07/2020 DUE FOR OPENING AT 03.30 HRS. ON 23.12.2020 and should be submitted at the following address up to 3.00 p.m. on or before 23.12.2020.

The Registrar,

NALSAR University of Law, Justice city,

Shameerpet, Hyderabad-500101.

QUALIFICATION CRITERIA OF BID – BID MAY BE REJECTED, BASED ON ANY ONE OF THE FOLLOWING REASONS :

- Only single Envelope (Technical Bid or Commercial Bid) received.

- Details received by fax.

- Unsigned Offer.

- If you mention Total Amount in “First Envelope – Technical Bid”. (Total Amount must appear in Annexure IV only).

- If your Organization does not have “PAN” issued by Income Tax authority.

- If the list of your existing Customers is NIL for this Item.

- If the bidder has not quoted for all the Items mentioned in this “Purchase Enquiry”.

- If the EMD (Bank Draft or Cash Receipt) is not kept in the first envelope.

CLARIFICATIONS:

a) For any technical clarification please contact:

Assistant Engineer,

Nalsar University of Law,

Post Box No.1, Justice City,

Shameerpet,  Medchal-Malkajgiri Dist,

HYDERABAD-500101

Tel.No. 040-23498110

Fax: 040-23498385/386.

NOTE: Registrar – NALSAR University of Law reserves the right to accept

or reject, in part or whole, any or all tenders received without assigning

any reasons whatsoever.

You are requested to confirm your intention to quote or regret to The Registrar,                 NALSAR University of Law, Justice city, Shameerpet, Hyderabad-500101.

Sd/-

REGISTRAR

NALSAR University of Law

SPECIFICATION   FOR  ANNUAL  MAINTENANCE   CONTRACT   FOR SEWERAGE TREATMENT PLANT   HAVING   CAPACITY   OF   150 KLD    AT   NALSAR UNIVERSITY OF LAW,SHAMEERPET, 500101.

S.No.	Description

1.	Minimum Manpower required per day:

i)	Operators 	03	Skilled (Each shift of 8 Hrs. one person)

The treated waste water should comply with the standards given in consent order by APPCB following parameters:

a)	PH. Value 			5.5 to 9.0

b)	Oil & grease 			Not to exceed 10 mg/L

c)	Suspended solids 		Not to exceed  100 mg/L

d)           Chemical Oxygen demand     	Not to exceed  250 mg/L

e)	BOD				Not to exceed 30 mg/L

f)	Temperature shall not to exceed 5 Degree Centigrade above the ambient Temperature of the receiving body.

2.	Terms & Conditions:

- The service should be offered round the clock, 365 days a year.

- All Tools & Tackles required should be provided by contractor.

- All disciplinary rules and regulations are to be followed by the work force of the Contractor during their stay at the premises, Uniforms and safety kits etc. have to be provided by the contractor only.

- All the materials spare parts, consumable such as oil, grease, chlorine etc. have to be provided by the contractor only.

- Consumables provided for smooth and effective functioning of the plant should be got approved by the Assistant Engineer and records must be enclosed with claim.

- Supplying and monitoring of hypochlorite at site.

- The Contractor should submit the preventive maintenance schedule for University approval and its implementation.

- The instruction given to the Contractor from time to time should be properly carried out and necessary records of action taken should be maintained in a Log Book.

- Any damages caused by the Contractor in existing facilities while carrying out the work shall be made good by the contractor to our entire satisfaction at their own risk and cost.

- All statutory requirements pertaining to the job etc. should be fulfilled by the contractor.

- No advance payment will be made to the Contractor. Monthly payments will be released after submission of bill after 30 days and satisfactory completion of job which is to be certified by the Engineer In-charge, NALSAR.

- Dismantled / replaced parts should be handed over to University Engineer.

- The party should submit copies of certificates of PF Code No. and registration under contract labour (Abolition / Regulation) Act, 1970 along with Tender documents and the Contractor having no such registration number, the necessary deductions will be made as per the Govt. Rules.

- All the contractor’s employees posted and working in University premises for the above mentioned work should be covered under ESIC making statutory contribution under ESIC Act and incase if the Contractor having no such registration the necessary deductions will be made as per the Govt. Rules.

- The Contractor should follow the guidelines, Rules & Regulation of the Labour Law while engaging labours.

- Under all circumstances, the sewage treatment plant should be maintained ina  pristine order by carrying out periodical check ups duly attending to the problems assured when encountered.

- The treated water should be colourless, odourless and should be worthy enough to be used for horticulture purpose (for maintaining of land scaping, lawns, etc., in the campus).

- Prompt and effective supervision such as change of oil, chlorine, carbon, sand and softener’s etc., must be carried out on regular basis.

- Work involves operation and maintenance of 150 cu. m. per day

- The Agency shall give assurance for the effluent treated water for its quality, i.e., colour, odourness and other standard parameters prescribed by APPCB and it should be fit for gardening purpose.

.	Special Conditions:

Name of the Work 			:    Operation and maintenance of 150 cu. m

Per day Sewage Treatment Plant,

Operation Time				:    24 Hours all 365 days.

Min. Man. Power required 		:    To be employed by the contractor for

the efficient running of the plant.

Operators Skilled 			:    03/Day (One person for each shift of

8 Hrs).

The Contractor should submit the names of the persons engaged for the work and they have to report to the Engineer-In-Charge of the Shift.  Persons employed should not be changed frequently and the every person employed for the work has to obtain proper Gate Pass from Security Department of the University as per the laid down procedures.

4.	Duties of Operators & Staff Employed:

Operation and the maintenance of system comprising of  Bar screen chambers,Aereation tank, lift pumps, motors, blowers, pipelines, setting tanks, filter unit, Chlorination tanks etc. together with the electrical panels and connections.  The Contractor has to keep the area of plant neat and clean.

5.	Repairs:

The Contractor has to do all minor repairs, for which no additional labour charges will be paid.    Under no circumstances plant should remain under breakdown for more than 03 hours.  In the event of breakdown/shut down the onus of attending to the problem in the shortest possible time will rest on the Contractor failing which Engineering Department is empowered to get the breakdown/shut down any defect rectified from any out side agency at the risk and cost of the Contractor and make necessary deductions from their bills.  The Contractor has to keep all the area and surroundings at the site neat and clean and dump the scrapped materials at the scrap yard.

It will be Contractor’s responsibility to maintain Sewerage Treatment Plant in good state all the time contractor should also to plan and undertake preventive maintenance of entire Sewerage Treatment Plant at regular intervals and attend routine maintenance activity every day.  Contractor should make a service report for all the maintenance jobs carried out and get it counter signed by the Engineer-in-charge.  The necessary registers/Documents will be maintained by the Contractor only.

The Contractor has to carry out necessary treatment to the sewage so as to get the following:

a)	PH. Value 			5.5 to 9		|  	As per the standard

b)	Oil & grease 			10   mg/L	|	limits of APPCB

c)	Suspended solids 		100  mg/L	|

d)	BOD				30    mg/L	|

e)	C.O.D. not to exceed 		250 mg/L	|

f)	Temperature shall not		5o C		|

exceed above the ambient

temperature of the receiving body.

Contractor has to carry out the testing of water at the interval of every month and whenever felt necessary as instructed to do so by the department and furnish the test reports to the Engineer-In-charge on priority.  The Contractor will also provide a Tests Certificate every month of effluent water before and after treatment and the certificate have to be obtained from the APPCB approved Lab. For B.OD, C.OD, PH, TSS, and O&G

It will be the responsibility of the Contractor to remove excess sludge from sludge holding tank. In addition, Contractor shall also carryout cleaning of Grease/Sludge holding Tanks periodically.  Any disposal of grease / sludge out side the premises will be borne by the party.

The Contractor shall supervise and maintain the ST Plant everyday and maintain a log book as per guidelines of the Operation Manual.

Once the contract is awarded to the successful contactor the EMD will be converted in to SD which will be free of interest and the same will be refunded to the Contractor only after the satisfactory completion of the contract.

All disputes will be under the jurisdiction of Hyderabad Court only.

6.  a)  It is the duty of contractor  to submit the test certificate from APSCL approved

labs before 5th of every month. In case the contractor fail to submit                                    the test certificate before 5th of every month Rs.6,000/-	 will be deducted from the

monthly payments.

b)  In case the contractor fails to provide the skilled operator at the work place more

than one hour in any day Rs.200/- per hour  will be deducted from the monthly

payments.t provided.

7.	Prequalification Criteria: The contractor should have completed during the last five years:

Average Annual Turnover during last 3 years, ending 31st March of previous Financial Year shall be at least Rs.6.00 lakhs.  The bidder’s financial capability shall be decided based on the average annual turn over and concurrent commitments.

8.   TERMINATION CLAUSE   :   The EMD will be converted into SD. The contractor can

be terminated by issuing 2 months’ notice from either

side.

*               *               *

ANNEXURE –I

ON TENDERER’S LETTER HEAD

C E R T I F I C A T E

To,

The Registrar,

Nalsar University of Law,

Post Box No.1,

Justice City,

Shameerpet,

Medchal-Malkajgiri Dist,

HYDERABAD-500101

Sir,

## It is certified that we have studied and understood the terms and conditions of the tender for AMC for Sewage Treatment Plant at NALSAR University of Law, Hyderabad.

The contractor is only the claim amount as per the amount quoted in Annexure –III.

The benefit of reduction in statutory taxes/ levies, if any, arising during the term of the contract, if awarded in our favour, would be passed on to NALSAR University of Law.

AUTHORISED SIGNATORY

COMPANY SEAL

ANNEXURE II

#### TECHNICAL BID FORMAT

TENDER NO. NALSAR/STP/07/2020

| 1 | Name of Contract |  |
| --- | --- | --- |
| 2 | Name of the Bidder / Co. |  |
| 3 | Address |  |
| 4 | Telephone No. / Mobile No. |  |
| 5 | Fax No. |  |
| 6 | Email ID |  |
| 7 | Name of Contact Person |  |
| 8 | The bidder must be in this or similar business for Maintaining Sewage Treatment Plant for the last one year. In case of authorized dealer, he must be in the similar business for the last one year. Please attach current authorization certificate. | Required Documentary proof submitted Yes / No |
| 9 | Attach photo copy of latest Income Tax Return |  |
| 10 | Sales Tax / TIN Number (Attach photo copy) |  |
| 11 | Attach photo copy of Annual Turnover for last two years |  |
| 11 | Certificate accepting all the terms and conditions unconditionally of the tender on the Bidder’s letter head in the format as given at Annexure- I. | Certificate accepting all the terms and conditions unconditionally of the tender on the Bidder’s letter head in the format as given at Annexure- I enclosed |
|  |  | YES / NO |
|  |  |  |  |  | YES / NO |
| 12 | Number of Employees | SKILLED | UNSKILLED |  |  |
| 13 | Details of institutional Customers.(Please attach proof) |  |  |  |  |
| 14 | PAN OR PF NO. (Please attach photo copy) |  |  |  |  |
| 15 | Mention all types of taxes considered/applicable i.e. VAT, Octroi, transportation, handling charges, insurance, etc. and their percentage. |  |  |  |  |
| 16 | Are you registered with N.S.I.C. ? (For details, visit www.nsic.co.in/go.asp ) If yes, please attach photo copy. |  |  |  |  |
| 17 | Attach photo copy of latest Electricity Bill of your Organization. |  |  |  |  |

AUTHORISED SIGNATORY & COMPANY SEAL

ANNEXURE - III

PRICE FORMAT

TENDER NO. NALSAR/STP/07/2020

Specification for AMC for ST Plant 150 KLD at NALSAR University of Law

| Sl. No. | Description | Qty. | Unit | Rate (Rs.) | Amount (Rs.) |
| --- | --- | --- | --- | --- | --- |
| 1 | Annual Operation & Maintenance Contract of Sewage Treatment Plant having capacity 150 Cum per day, with 3 Skilled Operators covering 24 Hours (i.e., 8 Hours each shift in all days). | 12 months | Month |  |  |

AUTHORISED SIGNATORY & COMPANY SEAL

ANNEXURE - IV

PRICE FORMAT

TENDER NO. NALSAR/STP/07/2020

Specification for AMC for ST Plant 150 KLD at NALSAR University of Law.

| Sl. No. | Description | Qty. | Unit | Rate (Rs.) | Amount (Rs.) |
| --- | --- | --- | --- | --- | --- |
| 1 | Replacement of Carbon media and sand media in containers of 150 KLD capacity STP all as specified and directed at site. | LS | 1 Job |  |  |
| 2 | Provision of iron ladder in place of old damaged with MS Angles including fabrication and applying of two coats of synthetic enamel paint over a coat of red oxide primer all as directed at site. | Kg’s | 50 |  |  |
| 3 | Replacement of Frontal pipeline required for PSF ACF tank as per existing dia & guage to 150 KLD capacities STP all as directed and specified at site. | Rmt | 30 |  |  |
| 4 | Repairs to Sludge transfer pumps including all accessories all as specified and directed at site. | Each | 02 |  |  |
| 5 | Provision of CBD FBD for air grid including any material required all as directed at site | LS | 1 Job |  |  |
| 6 | General Servicing to Blowers of 150 KLD capacity STP including all materials required to servicing like oil, grease, etc., all as specified and directed at site. | LS | 1 Job |  |  |
| 7 | Design to tube settler media as per directions to 150 KLD STP all as specified and directed at site | LS | 1 Job |  |  |
| 8 | Replacement of MBBR media to 150 KLD STP all as specified and directed at site. | Cum | 06 |  |  |
| 9 | M&L synthetic enamel paint over a coat of red oxide primer to all the equipment in STP Painting works to be required for all equipment’s. | Sqm | 100 |  |  |
|  | Total Amount |  |
| (Rupees only) |

NOTE:

1) Total amount shall exclude work contract tax, VAT, Service tax etc.

2) Do not attach any other sheet to this Annexure.

3) THE TENDERERS ARE ADVISED TO ENSURE THAT THE PRICES AND OTHER DETAILS ARE FILLED IN   CORRECTLY AND COMPLETELY IN THE ABOVE FORMAT.  SUBMISSION OF INCORRECT OR INCOMPLETE INFORMATION, AND / OR SUBMISSION OF THE ABOVE FORMAT WITH ARITHMETICAL ERRORS IN COMPLIATION OF THE DATA WOULD BE AT THE TENDERER'S SOLE RISK AND THE DECISION OF NALSAR IN SUCH CASES WOULD BE FINAL AND BINDING.

COMPANY SEAL

SIGNATURE 			                                      NAME        		______

DESIGNATION 		______                        MOBILE NO.